| 10 | 1 | PRIODOOR ETX RDA H Smoke damper, horizontal – according to EN 12101-8 Large format, single leaf, fire resistant smoke control damper especially designed for installation in air release shafts of RDA (RDA = Smoke protection pressure systems). The aim of the application is to keep safety staircases smoke-free. In case of fire the smoke control damper is opened automatically by the controls of the on-site RDA. Large-format cross-sections provide a clear, unobstructed air release area for fire gases. The closure is smoke-tight and provides fire resistance for 90 minutes. Function: Tested as a smoke damper Fire resistance 90 minutes Classification EI 120 (Ved - i↔o) S500C10000 AAmulti Smoke protection Tight seal Pressure / suction stable up to 500 Pa Sound reduction index depending on size up to 36 dB Construction: Single panel shaft closing with high mechanical durability Flush-fitting assembly in solid wall and PRIOWALL with assembly frames Free large format flow surface External construction width from 1000 mm to 2.100 mm External construction height from 379 mm to 1,000 mm Rebated wooden door casing without gas spring: three sides 64 mm, lock side 139 mm Rebated wooden door casing with gas spring: 2 x 64 mm and 2 x 139 mm All round smoke and fire protection seals, automatically foams in the event of fire High-quality stainless steel bands Gas springs depending on the size of the damper leaf included Subsequent, on-site painting of the smoke damper on the outside is possible. Drive: Opened and closed by chain drive System voltage 24 V DC Power consumption 40 mA, max. 1.2 A in cut-out torque With integrated adjustable limit switches Lock with power cut-off Chain drive adjusted by software Connector cable chain drive 6-pole, 3.00 m (2 conductors each for drive, limit and programming) Material characteristic: Non-combustible board with surface coating, classification A2 - s1, d0 Standard surface CPL Standard colour light grey - similar to RAL 7035, coloured edges and chamfers Green Building Declaration according to LEED and DGNB Scope of delivery: Smoke damper Assembly frame Chain drive with connector cable Attachment material Options: Inspection tool Commissioning set Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours Protective plate for smoke extraction flap Element-external dimensions (H x B) in mm: ………………………………….. Rough opening (H x B) in mm: ………………………………….. Surfaces: ………………………………….. Typ: PRIODOOR ETX RDA H Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |