| 10 | 1 | PRIOCEIL – 90 minutes Ceiling system Single-layer fire-resistant ceiling system with various surfaces for the formation of „room-in-room“solutions. The PRIOCEIL ceiling system consists of precise coated, non-flammable ceiling panels of 42 mm in thickness, which can be easily and neatly constructed, converted and expanded using connectors. As a component of the „System 42“ module fire protection system, PRIOCEIL can be combined with the PRIORIT wall system for the formation of rooms and is suitable for the installation of bulkheads or ventilation elements. PRIOCEIL is only offered in conjunction with complete PRIORIT solutions. Function 90 minutes fire resistance, fire resistant EI 90 a↔b/F 90 (above and below), classification Construction Single-layer, highly stable prefabricated elements with beams covering the joints. Project-related planning, production and installation Construction depth per element up to 1.20 m Connection to solid wall and/or PRIOWALL Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Green Building Declaration according to LEED and DGNB Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours PRIOCEIL is offered on a project-by-project basis Element-External dimensions (H x B) in mm: ……………..…………………….. Surface: …………..……………………….. Notice: ..………………………………….. ..………………………………….. ..………………………………….. ..………………………………….. Typ: PRIOCEIL 90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-210 |  |  |
| --- | --- | --- | --- | --- |