| 10 | 1 | PRIODOOR ETX A – 30 minutes Inspection opening closure, flush with the adjacent areas Inspection opening closure for flush mounting in GRP shaft walls with no visible frame. The lockable and sealed door with an aluminum frame that can be plastered over is suitable for compliant partitioning of small and large installation shafts and the partitioning of measuring equipment and distributors in escape and rescue routes. Quick and easy installation for easy access to shaft. The closure is tightly sealed all around and offers a fire resistance of 30 minutes. Function 30 minutes fire resistance, fire retardant EI 30 i→o, classification Flammability according to DIN 4102 Part 2 (ETK) over 30 minutes Tested fire behaviour from the inside of the chamber to the outside for at least 30 minutes, based on the standard fire in accordance with DIN 4102 Part 2 Compliance with temperature values max. 140 K on average, max. 180 K at points Verification of usability, technical group Z-6.55- Smoke protection Leak-proof closing Construction Inspection door with high mechanical resistance Flush mounting in 2 x 20 mm GRP shaft wall or 2 x 25 mm when planked Installed depth < 100 mm in metal stud wall Single-leaf design, Door stop position DIN right Circumferential aluminium frame with plaster edge Circumferential smoke and fire seals, expand automatically in the event of a fire Door closes flush with frame, opening angle ca. 180° Locking system with single cylinder Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Green Building Declaration according to LEED and DGNB Scope of delivery Door leaf with stainless steel hinges and box staple Aluminium frame, corner connection, fire and smoke seal Profile single cylinder Torque plate and fastening clip, Assembly blocks Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours Door lock cylinder rosette Profile single cylinder – simultaneous locking Element-External dimension (H x B) in mm: ………………………………….. Rough opening BRM (H x B) in mm: ………………………………….. Surface: ………………………………….. Wall type: ………………………………….. Options: ………………………………….. Typ: PRIODOOR ETX A 30 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |