| 10 | 1 | PRIODOOR ETX – 90 minutes Inspection opening closure for special solutions All-round tightly closing inspection opening closure for flush mounting in the installation shaft wall, optionally as shoring on the installation shaft wall. The closure is availabe single-leaf or doubl-leaf and is suitable for large-scale compliant partitioning of installation shafts and the partitioning of measuring equipment and distributors in escape routes. The closure is tightly sealed all around and offers a fire resistance of 90 minutes. Function 90 minutes fire resistance, fire resistant EI 90 i→o, classification Flammability according to DIN 4102 Part 2 (ETK) over 90 minutes Tested fire behaviour from the inside of the chamber to the outside for at least 90 minutes, based on the standard fire in accordance with DIN 4102 Part 2 Compliance with temperature values max. 140 K on average, max. 180 K at points Verification of usability, technical group Z-6.55- Smoke protection Leak-proof closing Construction Inspection opening closure with high mechanical resistance Flush mounting or for installation on the wall Single and double-leaf design Circumferential block frame 55 mm wide, 42 mm deep Circumferential smoke and fire seals, expand automatically in the event of a fire Door closes flush with frame, opening angle ca. 180° Single to triple latch lock, depending on door height Locking system with single cylinder Door stop position DIN right, optionally DIN left Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Green Building Declaration according to LEED and DGNB Scope of delivery PRIODOOR ETX as a kit Options PRIODOOR ETX with with three-sided frame and lowerable floor sealing PRIODOOR ETX-AW – Mounting on the wall Door handle set Automatic multipoint lock with panic function E Hinged ring handle Ventilation modul Mounting hardware for solid wall and GRP-shaft wall; flush installation Mounting hardware for solid wall and GRP-shaft wall; mounting on the wall Magnet Reed Contact Set Element-External dimension (H x B x T) in mm: ………………………………….. Rough opening (H x B) in mm: ………………………………….. Surface: ………………………………….. Wall type: ………………………………….. Three-sided frame and lowerable floor sealing: ………………………………….. Options: ………………………………….. Typ: PRIODOOR ETX 90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |