| 1 | 1 | PRIOWALL – 90 minutes Wall System Single-layer, fire-resistant wall system with various surfaces for the formation of interior partitions for room closures, fire areas, etc. The PRIOWALL wall system consists of coated non-flammable wall panels of 42 mm in thickness, which can be easily and neatly constructed, converted and expanded using various joining technologies. PRIOWALL is a component of the „System 42“ modular fire protection system and is suited for the installation of PRIORIT system components such as fire-protection closures, inspection opening closures, smoke-extraction flaps, fire dampers and bulkheads or ventilation elements. Function 90 minutes fire resistance, fire resistant EI 90 classification Construction Single-ply, highly stable prefabricated elements Construction possible in I-shape, L-shape and U-shape Planning on a project-by-project basis, manufacturing and installation Overall height up to 4 m, unlimited width Ceiling construction with PRIOCEIL Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Installation of System42 Components Wall system PRIOWALL Fire Resisting Closure PRIODOOR FSA Inspection Door PRIODOOR ETX / PRIODOOR RTX Smoke damper PRIODOOR ETX RDA (vertical/horizontal) Accessoires Fire protection glasses for inspection closure and door Cable and pipe bulk head for wall Ventilation systems for PRIOWALL / PRIODOOR ETX / PRIODOOR RTX Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours / veneer surfaces Element-external dimension (H x B) in mm: ……………..…………………….. Surface: …………..……………………….. Shape: ……….………………………….. Door stop (DIN L / DIN R): ………………….……………….. Number door leaf: ..………………………...……….. Number fixed leaf: ..………………………………….. Number traffic leaf: ..………………………………….. Number PRIODOOR ETX/RTX 1-flg.: ………………………………….. Number PRIODOOR ETX/RTX 2-flg.:………………………………….. Dimension PRIODOOR ETX/RTX 1-flg.: (H x B) in mm: …………………………………….. Dimension PRIODOOR ETX/RTX 2-flg.: (H x B) in mm: …………………………………….. Number PRIODOOR FSA 1-flg.: ..………………………………….. Dimension PRIODOOR FSA 1-flg.: (H x B) in mm ..………………………………….. Number PRIODOOR FSA 2-flg.: ..………………………………….. Dimension PRIODOOR FSA 2-flg.: (H x B) in mm ..………………………………….. Number PRIODOOR ETX RDA: ..………………………………….. Dimension PRIODOOR ETX RDA: (H x B) in mm ..………………………………….. Number PRIODOOR ETX RDA H: ..………………………………….. Dimension PRIODOOR ETX RDA H: (H x B) in mm ..………………………………….. More options Fire protection glasses: ..………………………………….. Dimension fire protection glasses: (H x B) in mm ..………………………………….. Cable and pipe bulk head: ..………………………………….. Ventilation systems: ..………………………………….. Notice: ..………………………………….. ..………………………………….. ..………………………………….. ..………………………………….. Typ: PRIOWALL 90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-210 |  |  |
| --- | --- | --- | --- | --- |