| 10 | 1 | PRIODOOR ETX TUN Tunnel Electro-Recess Closure Flush with the Adjacent Area Standardized, fire-resistant maintenance door, flush with the adjacent areas for the separation of safety-related relevant electrical installations in Tunnel niche. This door is suitable for securing the maintenance of performance function of safety-related electrical wiring systems and distributors for the emergency lighting and smoke clearance system. Design according to Directive 2004/54/EG, RABT, ZTV-ING Part 5. Function Fire resistance 90 minutes: fire-resistant EI 90/F 90 classification Smoke protection Safety class I Protection rating in accordance with IP 54 Stable against pressure / suction up to 1000 Pa Construction Single and double-leaf maintenance cover for flush installation in tunnel recess Fastening laterally inside with cable tie mount Door closes flush with frame Door opening angle ca. 90° Door hinges in stainless steel 1.4571 Turning lever in stainless steel 1.4401 prepared for DIN single cylinder Fire barrier with circumferential fire, smoke and dust proof seals Equipotential bonding Integrated door check strap With inductive proximity switch for door monitoring, 90° rotatable Material characteristic Building material with surface coating, classified A2 – s1, d0 non-combustible Building material and surface is chemically highly stable and moisture-resistant Outside surface in stainless steel 1.4571 Inside surface synthetic-coated Cable tie mount in stainless steel 1.4529 Door hinges in stainless steel 1.4571 Turning lever in stainless steel 1.4401 Scope of delivery Maintenance cover, fastening material, prepared for connection to equipotential bonding Options Outside surface powdered according to RAL Special sizes, special designs on request Lateral impact protection for front-panel mounting in the escape route Element-External dimension (H x B x T) in mm: ………………………………….. Rough opening (H x B) in mm: ………………………………….. Shape: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Wall type: ………………………………….. Door clearance height in mm: ………………………………….. Door clearance width in mm: ………………………………….. Options: ………………………………….. Typ: PRIODOOR ETX TUN Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |