| 10 | 1 | PRIOCAB Li EI90 Free-standing cabinet for the storage of lithium-ion batteries, 2-leaf PRIORIT free-standing housing, two-leaf type, suitable for smoke-tight and fire-resistant storage of lithium-ion batteries. The housing is made of noncombustible material, class A2 – s1, d0. The cabinets have a ventilation system in the rear panel and cable entries at the top and bottom as standard features. Function Fire resistance rating over 90 minutes Tested fire protection from the inside and outside Tested fire load insulation Suitable for the storage of lithium-ion batteries Construction Housing with high mechanical resistance Housing made of noncombustible material including the decorative surface Individual colour design Protection against unauthorised access – pivot lever with two-way cylinder All-round fire protection seal, intumescent in case of fire Top and bottom cable entry Integrated ventilation system, consisting of smoke detector and fan Cold smoke-tight closure system Smooth and easy, free-moving doors, inset type door, opening angle approx. 180° Accessible plinth (e.g. fork-lift forks), height 100 mm with removable plinth cover panel Four height-adjustable mesh shelves, load capacity 75 kg/floor Material characteristic Standard surface CP laminate is chemically highly stable and moisture-resitant Non-combustible board with surface coating, classified A2 – s1, d0 Surface light grey, similar to RAL 7035 Options Special decors / special colours Additional mesh shelf with 4 shelf supports, 30 x 1000 x 400 mm (H x W x D) Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Options: ………………………………….. Design variants ESL92.12444.BAT 4 Mesh shelves ESL92.12444.BAT01 4 Mesh shelves; 1 x 5-fold Power strip; Control unit ESL92.12444.BAT02 4 Mesh shelves; 4 x 5-fold Power strip; Fire extinguishing generator; Control unit Typ: PRIOCAB Li EI90 Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 210 |  |  |
| --- | --- | --- | --- | --- |