| 10 | 1 | PRIOCAB-Li Typ90 Safety cabinet for the storage of lithium-ion batteries Fire-resistant safety cabinet Type90 in two sizes: single-leaf cabinet with hydraulic door closer and a double-leaf cabinet with free-running doors including door closing mechanism. Suitable for storing lithium-ion batteries. The cabinets have exceptionally high stability and durability. The base material is highly compressed, non-absorbent and does not present a fire load. The floor-standing cabinets are equipped with a base that can be moved underneath as standard and can optionally be aligned with height-adjustable feet. Function Fire resistance rating (FWF) 90 minutes Safety cabinet type 90 according to EN 14470-1 Suitable for the storage of batteries Construction Housing with high mechanical resistance Housing made of noncombustible material including the decorative surface Individual colour design Single-leaf cabinet with hydraulic door closer, 90° hold-open, closure in case of fire Two-leaf cabinets with free-moving doors: thermally induced closure in case of fire Air supply and ventilation openings in the top of the cabinet are self-closing in case of fire, DN 100 mm connections Three height-adjustable pull-out trays, weight capacity 75 kg, hole spacing 32 mm Bottom tray with perforated sheet metal insert Accessible plinth (e.g. fork-lift forks), height 100 mm with removable plinth cover panel Integrated, height-adjustable feed for levelling out unevenness in the floor Material characteristic Standard surface CPL Non-combustible panel with surface coating, classified A2 - s1, d0 Standard surface light grey, similar to RAL 7035 Optionen Doors or entire corpus in alternative RAL colours / surfaces, on request. Fire-resistant cable bulkhead Additional tray bottom Single cable and pipe lead-through Smoke detector Exhaust air attachment Element external dimensions (H x W x D) in mm: ………………………………….. Surface: ………………………………….. Options: ………………………………….. Design variants EN91-196-060: Single-leaf safety storage cabinet with 3 shelves, 1 base tray with perforated sheet insert EN92:196-120: Double-leaf safety storage cabinet with 3 shelves, 1 base tray with perforated sheet insert Typ: PRIOCAB-Li Typ90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 / 3640 0 Fax : +49 6181 / 3640 210 |  |  |
| --- | --- | --- | --- | --- |