| 10 | 1 | PRIOCOVER Mobile fire protection cover Universally usable slip-on housing for comprehensive fire protection for active or passive storage of Lithium-ion batteries. The bottom opened case is provided with stable corner angles. The crane eyes allow easy transport and easy insertion. It is also possible to put the batteries over the case even if the fire starts. The fire protection cover has a fire resistance of 90 minutes. Function Non-combustible incl. decorative surface, A2-s1,d0 Fire resistant construction - Fire resistance 90 minutes Pressure Stable Mechanical pressure relief Expert opinion of an accredited material testing institute Suitable for passive and active storage User-friendly Easy handling Mobile, simple solution No time consuming putting the batteries in Safety cabinets Easy to put over loaded pallets Quick insertion by means of forklift truck Easy transport by means of crane eyes Corner angle edge protection Space-saving, stackable Standard size to cover a Euro pallet 1200 x 800 Covering of pallets, sump trays or mesh boxes Placement directly on existing floor Robust and durable Solid construction Edge and corner protection High stability High surface hardness High chemical resistance Scratch-resistant Stain resistant Single layer wall construction - wall thickness 42 mm Sustainability Recyclable Building material has Green Building Declaration according to LEED and DGNB Pollutant-free Material property Non-combustible board with surface coating, classified A2 – s1, d0 Standard surface CPL Standard colour light grey, similar to RAL 7035 Optional versions PRIOCOVER including fitting set for one cooling water connection PRIOCOVER including cable bulkhead for safe charging. The charging cables can remain on the floor. A fire protection stone safely seals the cables. PRIOCOVER including fitting set and cable bulkhead Accessories Building material with surface coating on both sides, classified A2 - s1, d0: non-combustible Standard surface CPL Standard colour light grey, similar to RAL 7035 Element external dimensions (H x W x D) in mm: ………………………………….. Surfaces: ………………………………….. Options: ………………………………….. Accessories: ………………………………….. Typ: PRIOCOVER Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |