| 10 | 1 | PRIODOC Typ92 – AS92:196-106-F-HRA-S Filing/Document Cabinets Double-leaf fire protection cabinet for the safe storage of files and documents. Made of non-combustible materials, the cabinet is also suitable for installation in escape and rescue routes. Function LFS 60 classification Smoke protection Suitability for secure storage of records Construction Body and doors made of solid material, inside and outside with decorative surface Double-leaf design Door closes flush with body, opening angle ca. 180° Automatic locking of non-active leaf if active leaf is closed Locking system with triple latch lock, profile semi-cylinder Smoke and fire seals, automatically expand in case of fire Vertically adjustable shelves in 32 mm grid Protection against external impacts from dust and dirt Material characteristic Non-combustible board with surface coating, classified A2 – s1, d0 Standard surface CP laminate Colour light grey, similar to RAL 7035, with ABS edges Scope of delivery PRIODOC 90 filing cabinet fully assembled on pallet Optionen All PRIORIT surfaces on request Additional shelves Vertical filing drawer including drawer guides Surface: ………………………………….. Options: ………………………………….. Typ: PRIODOC Typ92 AS92:196-106-F-HRA-S Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 210 |  |  |
| --- | --- | --- | --- | --- |