| 10 | 1 | PRIOLION Safety cabinet for lithium-ion batteries Fire-resistant safety cabinet, specially developed for the storage and charging of lithium-ion batteries. The safety cabinet, which was tested in accordance with test principle EK5/AK4 22-01 as well as in a real fire and GS (tested safety) certified, offers a fire resistance of 90 minutes both from the inside and the outside. This prevents a fire spreading from the inside to the outside as well as a burning of the critical stored goods in the event of a fire inside the installation site. A release of toxic fumes/gases in the event of a battery fire is prevented. Function Tested fire protection Tested fire resistance of 90 minutes from the outside to the inside according to DIN EN 14470-1 Max. temperature rise in the interior at no temperature measuring point more than 100 K Tested fire resistance of 90 minutes from inside to outside according to DIN EN 1363-2 GS mark - tested according to test principle EK5/AK4 22-01 Self-closing doors tested for continuous use Suitable for the storage and charging of lithium-ion batteries Internal real fire test of an equipped cabinet Structure & equipment Safety cabinet with high-quality surface inside and outside Permanently self-closing doors with oil-damped door closers Double-leaf version, double traffic leaf with centre bar Each door can be operated with one hand Cupboard doors close automatically from any position Doors lockable with profile cylinder (lockable) Incl. technical ventilation (to avoid heat accumulation in the interior) Closure of supply and exhaust air in case of fire, triggering via thermocouple and smoke detector Integrated pedestal that can be moved underneath, height 100 mm with removable pedestal cover, thus easy change of location possible Base cover included in scope of delivery Four height-adjustable gratings, max. load 75 kg/floor Integrated liquid-tight base tray (powder-coated sheet steel) to absorb any leakage that may occur. Each storage level can be equipped with a socket strip incl. 10 protective contact sockets Ready to plug in for connection to the mains supply With control unit as standard (visual and acoustic status indication) Smoke detector inside the cupboard automatically triggers in case of fire Optional fire suppression system A potential-free interface is available for connecting a signal (e.g. to a control centre). Complete disconnection of the power supply to the cabinet in the event of an emergency Overvoltage protection Material & surface Standard surface CPL Non-combustible panel with surface coating, classified A2 - s1, d0: non-combustible Standard surface light grey, similar to RAL 7035 Different decor surfaces on request Dimensions External dimensions H x W x D (mm): 2250 x 1212 x 664 Internal dimensions H x W x D (mm): 1687 x 1004 x 453 Scope of delivery PRIOLION Safety cabinet for active and passive storage of lithium-ion batteries 4 grid shelves Floor tray Control unit 230 V/AC Equipment variants Fire suppression system Socket strip (10 slots) Control unit 400 V/AC Power strips (number): ( 1 ( 2 ( 3 ( 4 Fire suppression system: ( yes ( no Accessories Mesh grid shelf with 4 shelf supports packed in a box EBEL-GSM telecommunication module, power supply unit, 2x CR123 batteries, SIM card, connection cable (1 m) with suitable plug for PRIOLION Options: ………………………………….. ………………………………….. Typ: PRIOLION LI92.195.120 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 / 3640 0 Fax : +49 6181 / 3640 210 |  |  |
| --- | --- | --- | --- | --- |