| 10 | 1 | PRIOPACK Storage container for safe storage of rechargeable lithium-ion batteries Storage containers for the storage of defective or damaged batteries with increased fire risk and for minimising the toxic fumes associated with a thermal runaway. The storage container is lined with a non-combustible thermal insulation material and has a fire resistance of 90 minutes. Additional filling and insulating material, which can absorb leaking electrolytes, completely encloses the Li-Ion batteries to be stored. This means that even with a thermal runaway - a chemical reaction with extreme heat development - the danger of fire spreading is prevented and the generation of toxic gases is minimised. Fire resistant storage containers Storage containers made of plastic Closure by means of hinged cover and snap lock Tight-closing cover Tight closure, including in case of fire – no lifting up of the cover Lined with a nonflammable thermal insulation material Colour grey Accessories Filler packs must be ordered separately. Recommended quantity depending on the size of the batteries 2 to 3 packs per box (one pack = 8 pieces) Element external dimensions (H x W x D) in mm: ………………………………….. Accessories: ………………………………….. Typ: PRIOPACK Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |