| 10 | 1 | PRIOBOX Fire Resistant Barrel Box Fire-resistant barrel cabinet for proper storage of flammable liquids in barrels up to 200 litres in size. Suitable as an extraction point for hazardous materials in the workplace. The homogeneous, solid material has high-quality, easy to clean interior and exterior surfaces. The base has sufficient clearance to drive a forklift underneath for transportation. Function Complies with the requirements of the Technical Regulations for Hazardous Material 510, Act on the Regulation of Matters Relating to Water, Hazardous Materials Safety Regulations, Ordinance on Installations Handling Materials Hazardous to Water Fire resistance 90 minutes: fire resistant Fire tested from the inside and the outside Expert opinion by an official material testing institute Construction & Equipment Drum cabinet with high mechanical resistance Single layer wall structure of homogeneous solid material Dimensions optimized for 200 litre drums with added pump 220 litre drain pan with grate for water pollution control according to the Water Resources Law § 19 Tilt resistant tank bottom, adjustable. With a central hole for systematic removal of leakage Lockable doors Door closer with hold-open system for automatic closing of doors in the event of a fire Ventilation openings on the top side, DN 100 - closure via fire dampers With ground clearance for easy lifting Material & Surface Standard surface CP laminate Building material with surface coating, classified A2 – s1, d0: non-combustible Surface light grey, similar to RAL 7035, edges and bevels in different colour Options Doors or entire body in alternative RAL colours / surfaces, on request Tank bottoms, max. load 75 kg Heavy duty shelf, max. load 100 kg Extract air attachment, ready to plug in Connection adapter set Aluminium fold-jointed bend pipe Cable and pipe compartment Single cable and pipe-penetration Assembly service Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Storage volume, number of drums: ………………………………….. Options: ………………………………….. Typ: PRIOBOX Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |