| 10 | 1 | PRIOCAB Typ30 Safety Cabinets according to DIN EN 14470-1 Fire-resistant type 30 safety cabinet, available in two sizes (single- and double-leaf) for proper storage of flammable liquids and solid materials in work areas. Type 30 safety cabinets, tested and approved in accordance with EN 14470-1, offer a fire resistance rating of 30 minutes, and are GS (geprüfte Sicherheit - tested safety) certified. The single-layer structure of the body and door give the cabinet a high level of mechanical strength. The high-quality interior and exterior surfaces are easy to clean. Feet are integrated as a standard feature and can be adjusted from the inside, making it easy to set up and align the cabinets. The base has clearance for a lift truck or forklift to drive underneath, allowing the cabinets to be moved and transported easily. Function Fire resistance 30 minutes GS Certificates Safety cabinet Typ30 according to EN 14470-1 Suitable for the storage of inflammable fluids Construction & Equipment Safety cabinet with high-quality surface inside and outside Single layer wall structure Available sizes: Single and double-leaf version (width 595 mm and 1195 mm) Self-closing ventilation openings at the cabinet top operate in the event of a fire, connections DN 100 mm Door closer with integrated hold-open system and thermocouples for automatic door closure in the event of fire Different equipment variants Fittings adjustable in 32 mm hole spacing Floor pan with perforated plate insert for use as a fourth storage level Grounded tank bottom, tilt resistant with a central hole for systematic removal of leakage With ground clearance for easy lifting, height 100 mm with removable front panel Material & Surface Homogeneous building material, single-layer construction Standard surface CP laminate Surface light grey, similar to RAL 7035 Easy to clean Options Doors and entire body in alternative RAL colours / surfaces, on request Tank bottoms, max. load 75 kg Fully extendable shelf, max. load 75 kg Load increase to 150 kg Floor pan incl. perforated plate insert Perforated plate insert Equipment in stainless steel on request Fine (pre)filter for EBEL:VENT-EN-U (replacement) Replacement active charcoal filter for EBEL:VENT-EN-U Connection adaptor for EBEL:VENT-EN-U Recirculated air attachment, ready to plug in Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Options: ………………………………….. Typ: PRIOCAB Typ30 Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |