| 10 | 1 | PRIOCAB Typ90 - double-leaf Under-table safety cabinet according to DIN EN 14470-1 Fire resistant, double-leaf under table type 90 safety cabinet for proper storage of flammable liquids and solid materials in work areas. Type 90 safety cabinets, tested and certified in accordance with EN 14470-1, offer a fire resistance rating of 90 minutes, and are GS (geprüfte Sicherheit - tested safety) certified. The cabinets offer an extraordinary level of stability and a long service life. The base material is high-density, and does not represent a fire load. The high-quality interior and exterior surfaces are easy to clean. The doors of the safety cabinets close automatically in case of a fire. Function GS Certificates Fire resistance 90 minutes Safety cabinet Typ90 according to EN 14470-1 Suitable for the storage of inflammable fluids Construction & Equipment Under-table safety cabinet with high-quality surface inside and outside Single-layer doors and walls made of homogeneous solid material Double-leaf version (width 1100 mm) In case of fire, self-closing ventilation openings at the rear, connections DN 100 mm Free-wheeling doors with thermally induced closure in case of fire Different equipment variants Fittings adjustable in 32 mm hole spacing Floor pan with perforated plate insert for use as a fourth storage level Grounded tank bottom, tilt resistant with a central hole for systematic removal of leakage Material & Surface Standard surface CP laminate Building material with surface coating, classified A2 – s1, d0: non-combustible Surface light grey, similar to RAL 7035 Options Doors and entire body in alternative RAL colours / surfaces, on request Tank bottoms, max. load 75 kg Fully extendable shelf, max. load 75 kg Load increase to 150 kg Floor pan incl. perforated plate insert Perforated plate insert Fine (pre)filter for EBEL:VENT-EN-U (replacement) Replacement active charcoal filter for EBEL:VENT-EN-U Single cable and pipe-penetration Recirculated air attachment, ready to plug in Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Options: ………………………………….. Typ: PRIOCAB Typ90 – Under-table Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |