| 10 | 1 | PRIOCAB Typ90 - single-leaf Safety Cabinets according to DIN EN 14470-1 Fire-resistant type 90 safety cabinet for proper storage of flammable liquids and solid materials in work areas. Type 90 safety cabinets, tested and certified in accordance with EN 14470-1, offer a fire resistance rating of 90 minutes, and are GS (geprüfte Sicherheit - tested safety) certified. The cabinets offer an extraordinary level of stability and a long service life. The base material is high-density, and does not represent a fire load. The high-quality interior and exterior surfaces are easy to clean. Feet are integrated as a standard feature and can be adjusted from the inside, making it easy to set up and align the cabinets. The base has clearance for a lift truck or forklift to drive underneath, allowing the cabinets to be moved and transported easily. The doors of the safety cabinets close automatically in case of a fire. Function GS Certificates Fire resistance 90 minutes Safety cabinet Typ90 according to EN 14470-1 Suitable for the storage of inflammable fluids Construction & Equipment Safety cabinet with high-quality surface inside and outside Single-layer doors and walls made of homogeneous solid material Single leaf version (width 595 mm) Self-closing ventilation openings on the top of the cabinet operate in the event of fire, connections DN 100 mm Single leaf cabinet with hydraulic door closer, mechanical hold-open 90° and closing in the event of fire Different equipment variants Fittings adjustable in 32 mm hole spacing Floor pan with perforated plate insert for use as a fourth storage level Grounded tank bottom, tilt resistant with a central hole for systematic removal of leakage With ground clearance for easy lifting, height 100 mm with removable front panel Material & Surface Standard surface CP laminate Building material with surface coating, classified A2 – s1, d0: non-combustible Surface light grey, similar to RAL 7035 Options Doors and entire body in alternative RAL colours / surfaces, on request Tank bottoms, max. load 75 kg Fully extendable shelf, max. load 75 kg Load increase to 150 kg Floor pan incl. perforated plate insert Perforated plate insert Equipment in stainless steel on request Fine (pre)filter for EBEL:VENT-EN-U (replacement) Replacement active charcoal filter for EBEL:VENT-EN-U Single cable and pipe-penetration Recirculated air attachment, ready to plug in Extract air attachment, ready to plug in Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Options: ………………………………….. Typ: PRIOCAB Typ90 – single-leaf Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |