| 10 | 1 | PRIOCAB Typ90 Under-table pull-out units according to DIN EN 14470-1 Fire resistant under table type 30 pull-out cabinet for proper storage of flammable liquids and solid materials in work areas. Type 90 safety cabinets, tested and certified in accordance with EN 14470-1, offer a fire resistance rating of 90 minutes, and are GS (geprüfte Sicherheit - tested safety) certified. The cabinets offer an extraordinary level of stability and a long service life. The base material is high-density, and does not represent a fire load. The high-quality interior and exterior surfaces are easy to clean. The doors of the safety cabinets close automatically in case of a fire. Function GS Certificates Fire resistance 90 minutes Safety cabinet Typ90 according to EN 14470-1 Suitable for the storage of inflammable fluids Construction & Equipment Safety cabinet with high-quality surface inside and outside Single-leaf doors and walls made of solid homogeneous material Available in three different versions (width 592 mm and 1100 mm, 1100 mm with two pull-outs) Self-closing ventilation and exhaust opening in case of fire on the rear side of the cabinet, connections DN 100 mm Free-moving drawer with locking function in case of fire Certified, flame-resistant pipe penetrations for use as unloading/disposal station Earthing terminal for safely transferring hazardous substances Lockable with cylinder lock including closure-status indicator Cabinet is equipped with rollers for easy on-site movement Material & Surface Standard surface CP laminate is chemically highly stable and moisture-resitant Building material with surface coating, classified A2 – s1, d0: non-combustible Surface light grey, similar to RAL 7035 Options Doors and entire body in alternative RAL colours / surfaces, on request Recirculated air attachment, ready to plug in Fine (pre)filter for EBEL:VENT-EN-U (replacement) Replacement active charcoal filter for EBEL:VENT-EN-U Version Under-table safety cabinet with one pull-out Under-table safety cabinet with two pull-outs Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Options: ………………………………….. Typ: PRIOCAB Typ90 – Under-table pull-out safety cabinet Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |