| 10 | 1 | PRIOCONT Fire-Resistant Container Fire-resistant container to store two IBC containers or six 200l barrels on Euro pallets. The homogeneous, solid material has high-quality, easy to clean interior and exterior surfaces. The base has sufficient clearance to drive a forklift underneath for transportation. The container is smoke proof in accordance with DIN 18095 and offers a fire resistance of 90 minutes. Function Complies with the requirements of the Technical Regulations for Hazardous Material 510, Act on the Regulation of Matters Relating to Water, Hazardous Materials Safety Regulations, Fire resistance 90 minutes: fire resistant EI 90/F 90 classification Expert opinion by an official material testing institute Construction & Equipment Container of high mechanical resistance Single layer wall structure of homogeneous solid material Galvanized base drip pan for environmental protection according to the Water Resources Law § 19 Dimensions optimized for IBC containers and Euro palettes Door(s) with 3D stainless steel strips, 3-point locking system and profile semi-cylinder Electrical door hold-open system with flexible and adjustable door opening angle up to 120° Smoke triggered fire detection for automatic door closure Closing sequence control Explosion-protected electrical system Ventilation openings on the top side, DN 100 - closure via fire dampers Shelves with hot-dip galvanised grates Type PRIOCONT 2-IBC Material & Surface Standard surface CP laminate Building material with surface coating, classified A2 – s1, d0: non-combustible Colour light grey, similar to RAL 7035 Scope of delivery Sump Tandem door closer Door coordinator incl. door damper Options Doors or entire body in alternative RAL colours / surfaces, on request Design with anti-burglary protection according to WK 2 Fire-resistant cable compartment Single cable and pipe-penetration Panic hardware with panic function B “standard” Assembly on-site Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Storage volume number IBC: ………………………………….. Storage volumen number euro palette: ………………………………….. Storage volumen number drums: ………………………………….. Options: ………………………………….. Typ: PRIOCONT Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |