| 10 | 1 | PRIOROOM GAS Fire-resistant safety cell Special solution for gas cylinder storage Compact, fire-resistant safety cell for safe storage of gas cylinders. The safety cell can be constructed quickly and cleanly in custom dimensions made of pre-fabricated elements that are just 42 mm in thickness, in consideration of the existing building structures. It offers a fire resistance of 90 minutes. A steel cylinder truck can be used to drive into the safety cell on ground level or via an approach ramp. The homogeneous, solid material has high-quality, easy to clean interior and exterior surfaces. The safety cell has undergone an expert assessment by an accredited materials testing institute, and offers certified quality. It is an alternative to commonly available gas cylinder cabinets. Function Fire resistance 90 minutes: fire resistant Expert opinion by an official material testing institute Construction & Equipment High mechanical resistance Barrier-free entry with transport equipment possible Door(s) with 3D stainless steel strips, 3-point locking system, prepared for profile cylinder Suitable for the storage of compressed gas cylinders Ventilation openings on the top side, DN 100 - closure via fire dampers Material & Surface Building material with surface coating on both sides, classified A2 – s1, d0 non-combustible Standard surface CP laminate Colour light grey, similar to RAL 7035 Options Doors or entire body in alternative RAL colours / surfaces Fire resistant cable compartment Barrier-free access on request Ventilaton flap Base with toeboard Fire-resistant gas cylinder walk-in storage units, 1-leaf GFR91:600 for 2 x 50 litres / 3 x 10 litres gas cylinder GFR91:800 for 3 x 50 litres / 5 x 10 litres gas cylinder Fire-resistant gas cylinder walk-in storage units, 2-leaf GFR92:1200 for 4 x 50 litres / 7 x 10 litres gas cylinder GFR92:1400 for 4 x 50 litres / 8 x 10 litres gas cylinder Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Door stop (DIN L / DIN R): ………………………………….. Number door: ………………………………….. Door clearance height in mm: ………………………………….. Door clearance width in mm: ………………………………….. Number door leaf: ………………………………….. Number fixed leaf: ………………………………….. Number active leaf: ………………………………….. Storage volumen number of gas cylinder: ………………………………….. Options: ………………………………….. Typ: PRIOROOM GAS Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |