| 10 | 1 | PRIOROOM FRI Fire resistant room, individual Fire-resistant and individually designable room, consisting of 42 mm thick prefabricated, non-combustible individual components wall, ceiling, fire protection closure („System42“) as well as bulkheads and ventilation elements. The room (consisting of walls and ceilings of fire resistance duration F90 and T90 doors) offers a fire resistance of 90 minutes and can be constructed as a room formation in a quick and clean construction method, taking into account the existing building structure and connection to structural conditions. Function Fire resistance 90 minutes, fire resistant Walls: F 90/EI 90 classification Ceiling: F 90/EI 90 a↔b T 90-RS Classification of door(s) Door(s) smoke-tight, continuous function tested Optional fire resistant cable bulkhead - classification S90 Optional fire-resistant cable/pipe bulkhead Optional supply/exhaust air system NW 100 mm - classification K90 Construction Individual room with high mechanical resistance Fire protection through the creation of a separate fire compartment Break-in door, self-closing Door can be unhinged, lever handle set in stainless steel Door(s) with 3D stainless steel hinges and 3-way locking, prepared for profile half cylinders Doors with all-round fire and smoke protection seals Material characteristic Non-combustible board with surface coating, classified A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour System42 Components Wall system PRIOWALL Fire Resisting Closure PRIODOOR FSA Ceiling system PRIOCEIL Options and accessories Standard colours - white, similar to RAL 9016, decor brushed aluminium, primer foil Special decors, special colours Panic lock Cable and pipe bulkheads, rectangular or round Shut-off device with thermal release PRIOROOM is offered on a project-by-project basis Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Number door: ………………………………….. Door clearance height in mm: ………………………………….. Door clearance width in mm: ………………………………….. Options: ………………………………….. Typ: PRIOROOM FRI individual Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |