| 10 | 1 | PRIOELEC EK – 30 minutes Electro Terminal Box without Equipment Fire protection electro terminal box as empty housing for mounting on wall for the installation of hardware and safety fuses. Proof of functional integrity must be provided in accordance with MLAR. Function 30 minutes fire resistance, fire retardant Classification: Suitable for maintenance of performance for 30 minutes Construction Cabinet with high mechanical resistance for surface mounting Mounting via four holes in the frame corners Cover with recessed grip and bolted down with two self-locking nuts Demountable frame plate system for easy cable entry Cables can be inserted from two opposite sides Cable bulkheads automatically expand in the event of a fire Simple mounting of installations via pre-drilled holes Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Surface CP laminate Color light grey, similar to RAL 7035, edges and bevels in different color Installation Easy installation and cable management via demountable frame plate system in sandwich architecture Element-External dimension (H x B x T) in mm: ………………………………….. Weight: ………………………………….. Wall type: ………………………………….. Options: ………………………………….. ………………………………….. Typ: PRIOELEC EK30 (without Equipment) Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |