| 10 | 1 | PRIOELEC EW – 90 minutes Electro Wall Recessing Cabinet PRIORIT electro wall recessing cabinet in single-leaf design, suitable for maintenance of performance of safety systems in the event of fire for 90 minutes. The body is made of non-combustible building material class A2 – s1, d0. As a standard, cabinets are prepared for cable entries from top and bottom. The inside dimensions are based on the standard distribution panels. Proof of functional integrity must be provided in accordance with MLAR. Function Fire resistance of 90 min, fire resistant Classification: Suitable for maintenance of performance for 90 minutes Smoke protection Construction Empty case for wall recessing Door can be unhinged Door hinge right, may be changed on site to the left Door closes flush with body, opening angle ca. 180° 2-point door locking with swing lever and double-bit cylinder Circumferential fire seals automatically expand in the event of a fire Cable entry top + bottom Fastening system for electric installations Material characteristic Non-combustible board with surface coating, classified A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours EDF fixing cross beam Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Door hinge (DIN L / DIN R): ………………………………….. Panel height: ………………………………….. Panel width: ………………………………….. Unit space: ………………………………….. Options: ………………………………….. Typ: PRIOELEC EW90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |