| 10 | 1 | PRIODOOR RTH – 90 minutes Inspection Opening Closure Universally applicable, smoke-tight inspection opening closure for installation in solid and GKF shaft walls. The single-leaf inspection closure is suitable as a large-format closure of inspection openings in fire-resistant installation shafts and thus offers the possibility of the best possible accessibility of technical installations. The requirements for inspection closures according to the Model High-Rise Building Directive with regard to fire resistance, smoke tightness and self-closing are fulfilled. Function Fire resistance 90 minutes, fireproof Compliance with the maximum temperature increase in accordance with DIN 4102 Part11 – 180 K Flammability according to DIN 4102 Part 2 (ETK) over 90 minutes Tested fire behaviour from the inside of the chamber to the outside for at least 90 minutes, based on the standard fire in accordance with DIN 4102 Part 2 Compliance with temperature values max. 140 K on average, max. 180 K at points Verification of usability, technical group Z-6.55- Smokeproof Self-closing Fire-tested from the inside and the outside Non-combustible including the decorative surface A2 - s1, d0 Sound reduction index depending on size up to 37 dB Construction Single-leaf inspection hatch cover With internal overhead door closer Angle of opening up to 120° Flush-mounted profile half-cylinder – lockable from the outside Stainless steel piano hinge Right-hinged DIN door Wraparound block frame Installation Flush mounting Central installation Flush installation in solid walls Installation in solid walls Installation in GKF shaft walls Installation flush with floor or raised Ready for installation ex works Pre-assembly (max. 20 mm) to create a uniform plaster surface Material characteristic Non-combustible material with surface coating, classification A2 – s1, d0 Standard surface is laminate Standard colour is light grey – similar to RAL 7035, edges and chamfers in contrasting darker colour Scope of delivery PRIODOOR RTH in kit form Black wrist strap Options Various PRIORIT surfaces Priming film - can be painted on-site Aluminium decor Without overhead door closer Magnet Reed Contact Set Element external dimensions (H x W x D) in mm: ………………………………….. Basic dimensions (H x w) in mm: ………………………………….. Surface: ………………………………….. Wall type: ………………………………….. Type of installation: ………………………………….. Options: ………………………………….. Typ: PRIODOOR RTH 90 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |