| 10 | 1 | PRIOCOPY Printer and Copier Housing Housing made of fire-resistant components, consisting of non-combustible boards with surface A2 – s1,d0 and a material thickness of only 42 mm. Industrially prefabricated housing for printers and copiers in extra-wide corridors and aisles. Benefits: free access to the devices, self-closing slidingdoors in the event of smoke and fire, high-quality optics with chemical-resistant surfaces, fast setup and non-destructive disassembly. Function 90 minutes fire resistance, fire resistant Construction Copier enclosure consisting of copier cell and adjacent side cabinets Copier cell with two sliding doors, lockable Side cabinets with single leaf doors, lockable Door opening angle of side doors ca. 90° Side doors close flush with body, door handle set with catch lock, stainless steel bands, can be unhinged Sliding doors automatically close in the event of smoke and fire Doors with smoke and fire seals Junction box on the back wall (safety plug with grounding provisions) 8 shelves, load per shelf 75 kg Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Scope of delivery Copier enclosure disassembled on pallets, smoke detector, interior lights, 8 shelves, 2 switches, 2 wall sockets, door handles Options Standardised colours; brushed aluminium decor; primer foil Special decors / special colours Element-External dimension (H x B x T) in mm: ……………………………………. Surface: ……………………………………. Weight: ……………………………………. Options: ……………………………………. Typ: PRIOCOPY Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |