| 10 | 1 | PRIODOOR EVX – 30 Minutes Fire protection barrier, Surface-Mounted Universally usable fire protection barrier with installation frame for easy wall installation. The fire protection barrier is ideally suited for the small-surface to large-scale bulkheading of in-wall and panel distributors in rescue routes. The closure is tightly sealed all around and offers a fire resistance of 30 minutes. Function 30 minutes fire resistance, fire retardant Smoke protection Construction Fire-protection barrier for full-surface wall installation With circumferential, pre-drilled mounting frame, 22 mm material thickness, 115 mm wide Mounting on solid wall 2-point door locking device with turning lever and single cylinder, can be integrated into the building locking system Single leaf door with stop position DIN right Double-leaf design up to H x W 2500 mm x 2300 mm Circumferential smoke and fire seals, automatically expand in the event of a fire Mounting directly on the wall with pre-drilled holes in mounting frame Door leaf easy to hinge and unhinge Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Green Building Declaration according to LEED and DGNB Scope of delivery PRIODOOR EVX with mounting frame Mounting hardware for solid wall Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours Up to 3-fold doubling of the frame to cover protruding elements Element-External dimension (H x B x T) in mm: ………………………………….. Rough opening (H x B) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Wall type: ………………………………….. Options: ………………………………….. Typ: PRIODOOR EVX Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |