| 10 | 1 | PRIODOOR – 30 Minutes Fire Resisting Closure Single leaf and double leaf doors (fire resisting closures) with block frames and circumferential smoke seal, decorative surface or real wood veneer. With general building authority approval. Function 30 minutes fire resistance, fire retardant T 30-RS classification Smoke-tight and tested for continuous operation Soundproofing 37 dB (1-leaf) Construction Fire door with high mechanical resistance Standard door height up to 2,500 mm Standard double-leaf door width up to 2,500 mm Hydraulic door closer for automatic door closure Three-sided block frame, 55 mm thick and made of the same solid material Grooved door, closes flush with the block frame on both sides Circumferential and permanently elastic smoke seal Circumferential fire protection seal, automatically expands in case of fire 3D stainless steel bands, latch lock with double cylinder Smokeproof design with floor sealing Material characteristic High density solid material with high mechanical resistance Standard HPL surface Standard design: white - similar to RAL 9016; Edges and chamfers darkly contrasted Green Building Declaration according to LEED and DGNB Options and accessories Standardised colours - decor aluminium brushed; primer foil Surfaces in alternative RAL colours, decors or real wood on request Surface in stainless steel and thin sheet on request Double-leaf doors with asymmetrical door leaf division Extra wide frames according to requirements Floor seal, self-extending for smoke protection Flush fitted fire protection glazing Lock with panic release for emergency exits PRIODOOR is offered on a project-by-project basis Element-External dimension (H x B) in mm: ………………………………….. Rough opening: (H x B) in mm: ………………………………….. Surface: ………………………………….. Wall type: ………………………………….. Door hinge (DIN L / DIN R): ………………………………….. Number glas elements: ………………………………….. Dimension glas elements ………………………………….. (H x B) in mm: Number fixed leaf: ………………………………….. Number active leaf: ………………………………….. Options: ………………………………….. Typ: PRIODOOR FSA 30 T 30-1-FSA "PRIODOOR T31" T 30-1-RS-FSA "PRIODOOR T31“ T 30-2-FSA "PRIODOOR T32" T 30-2-RS-FSA "PRIODOOR T32" Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |