| 10 | 1 | PRIOELEC EW – 30 Minutes Electro Wall Recessing Cabinet PRIORIT electro wall recessing cabinet in single-leaf design, suitable for a smoke-tight and fire-resistant separation of electrical distributors in rescue routes (fire load insulation). The housing is made of non-combustible building material class A2 – s1, d0. As a standard the cabinets have top and bottom cable entries. The inside dimensions are based on the electro-technical standard distribution panels and mounting plates. Function Fire resistance of 30 min, fire-retardant Classification: suitable for fire load insulation of 30 minutes Smoke protection Construction Empty case for wall recessing Door can be unhinged Door hinge right, may be changed on site to the left Door closes flush with body, opening angle ca. 180° 2-point door locking with swing lever and double-bit cylinder Circumferential fire seals automatically expand in the event of a fire Cable entries top + bottom Attachment points for electric installations Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours EDF fixing cross beam Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Door hinge (DIN L / DIN R): ………………………………….. Panel height: ………………………………….. Panel width: ………………………………….. Unit space: ………………………………….. Options: ………………………………….. Typ: PRIOELEC EW30 Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |