| 10 | 1 | PRIOHYD Integral Shaft Enclosures for Fire Extinguishing Equipment DIN 14461 A standardised fire and smoke protection system for the installation of fire extinguishing equipment per DIN 14461 has become available for vertical shafts for the first time: wall hydrants, discharge points and feed-in systems can be simply and quickly placed directly into the shaft wall with PRIOHYD without further panelling. Function Fire resistance of 90 minutes For Extinguisher hose installations and wall hydrants according to DIN 14461 Non combustible composite material, classified A2 – s1, d0 Protection against drafts, cold smoke and hot combustion gases Proof of expert opinion Construction Housing with high mechanical resistance Fire protection with consistent installation into GRP shaft wall Seal-off of the extinguisher technology from the service shaft PRIOHYD without glass door for installing built-in steel wall cabinets with extinguisher technology from various manufacturers PRIOHYD with optional inspection cover for entry into the shaft and inspection of riser cables and technology Extinguisher technology’s weight transfer to storey floor Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Standard colour light grey - similar to RAL 7035, coloured edges and chamfers Scope of delivery Corpus Fire stop cuff for joining pipe Transportation aid for easy installation by using a jack lift Installation Instruction Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Wall type: ………………………………….. Fire alarm: ………………………………….. Hose reel / Extinguishers / Discharge points: ………………………………….. Options: ………………………………….. ………………………………….. Typ: PRIOHYD Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |