| 10 | 1 | PRIOROOM Fire Resistant Storage Room Fire-resistant space of non-combustible A2 building material for the construction of storage and service areas required by building regulations: theatre/props– sales areas/waste – escape and rescue routes/vending machines and others. With only 42 mm panel thickness, the room offers a space-saving alternative to conventional solid construction. Benefits: chemically highly stable, decorative internal and external surface, fast and clean to install, extensible, can be re-configured. The room is smoke-tight and provides 90 minutes fire resistance. Function Fire resistance 90 minutes: fire-resistant Wall: EI 90 classification Ceiling: F 90/EI 90 a→b T 90-RS classification of door(s) Door(s) are smoke-tight, tested for continuous operation Construction Room with high mechanical resistance Fire protection through the formation of a separate fire compartment Protection against fire from inside and outside Modular design of prefabricated parts Overall height up to 4,000 mm, overall width up to 6,500 mm and unlimited depth Door height and width up to max. 2,500 mm Door(s) with 3D stainless steel bands, opening angle ca. 170° Door(s) with hydraulic door closer, triple locking system, prepared for single cylinder Fire-resistant vents K90 NW 100 mm, freely positionable within the wall elements Fire resistant cable bulkhead 125 mm diameter, 60% assignable, freely positionable within the wall elements Room can be equipped with lighting, ventilation, shelves and fire protection bulkheads Material characteristic Non-combustible board with surface coating, classification A2 – s1, d0 Standard CPL surface Colour light grey, similar to RAL 7035, edges and bevels in different colour System42 Components Wall system PRIOWALL Fire Resisting Closure PRIODOOR FSA Ceiling system PRIOCEIL Options Standardised colours - white, similar to RAL 9016; decor brushed aluminium; primer foil Special decors / special colours Doors and/or walls in alternative RAL colours, decorative and veneer surfaces Single-leaf, double-leaf doors freely positionable Panic lock with panic function B Door closers Door hold-open system Smoke Detector Cable and pipe bulkhead Fire protection glass for inspection doors and doors Ventilation flap Fire damper PRIOROOM is offered on a project-by-project basis Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Number door: ………………………………….. Door clearance height in mm: ………………………………….. Door clearance width in mm: ………………………………….. Options: ………………………………….. Typ: PRIOROOM Fabrikat: PRIORIT AG www.priorit.de Tel.: +49 6181 3640-0 Fax : +49 6181 3640-230 |  |  |
| --- | --- | --- | --- | --- |