| 10 | 1 | PRIOROOM IT / PRIOROOM IT+ Fire-Resistant Room Fire-resistant room for the basic protection of IT, communication, and network systems. With just 42 mm panel thickness, the room offers space-saving room-in-room alternatives to conventional interior work of solid construction. The benefits: Can be quickly and cleanly installed, expanded, and retrofitted during ongoing opera-tion. The PRIORIT 42 mm system’s modular construction allows multiple alternatives with fire- and smoke-protected ventilation systems, valves, and fittings. The room offers 90 min. of fire re-sistance. PRIOROOM IT+ is lined inside with low-temperature insulation and provides increased IT protection based on EN 1047-2. Function 90 minutes fire resistance, fire resistant EI 90/F 90 classification walls/ceiling T 90 RS classification of door(s) Smoke-tight doors, tested for continuous operation Protection rating according to IP 54. PRIOROOM IT+ Limits according to EN 1047-2 Construction Room with high mechanical and thermal resistance Fire protection by forming a separate fire protection section External and internal fire protection Overall height up to 4,000 mm, overall width up to 6,500 mm and unlimited depth Door height and width up to max. 2,500 mm Door(s) with 3D stainless steel bands, 3-point locking system and profile semi-cylinder Design for raised-floor design possible PRIOROOM IT+ 42 mm internal insulation of walls and door(s) Material characteristic Building material with surface coating on both sides, classification A2 – s1, d0 non-combustible Standard surface CP laminate is chemically highly stable and moisture-resitant Colour light grey, similar to RAL 7035, edges and bevels in different colour Options Strike plates, door handles, rosettes Door closer Door hold-open system Ventilation, cable and pipe bulkheads Pipe system for connection to on-site ventilation system on request Stainless steel encasement 1.4571 on request Ventilation flap PRIOROOM IT are offered on a project-by-project basis. Element-External dimension (H x B x T) in mm: ………………………………….. Surface: ………………………………….. Number of doors: ………………………………….. Door clearance height in mm: ………………………………….. Door clearance width in mm: ………………………………….. Number of door leaf: ………………………………….. Options: ………………………………….. Typ: PRIOROOM IT Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |