| 10 | 1 | PRIOWALL IT / PRIOWALL IT+ Fire-Resistant Wall and Door System Wall and door system with glass elements for the fire-resistant separation of IT, power supply and ventilation/fire extinguishing equipment into independent fire zones. The wall and door system is cold and hot smoke-tight and provides fire resistance for 90 minutes. The high-quality interior and exterior surfaces round off the neat appearance of this easily, quickly and cleanly installable and expandable wall system. The 42 mm modular design allows a variety of alternatives to fire-safe ventilation systems, cable/pipe bulkheads, valves and fittings. PRIOWALL IT+ is trimmed with a low-temperature insulation and provides increased IT protection on the basis of EN 1047-2. Function 90 minutes fire resistance, fire resistant EI 90/F 90 classification of wall T 90 RS classification of door(s) Smoke-tight door(s), tested for continuous operation PRIOWALL IT+: Limits according to EN 1047-2 in connection with existing spatial elements and comparable properties Construction Room with high mechanical and thermal resistance Fire protection by forming a separate fire protection section Protection against fire from one side Overall height up to 4,000 mm, any width Suitable for door heights up to H x W 2,500 x 2,500 mm Door(s) with 3D stainless steel bands, 3-point locking system and profile semi-cylinder PRIOWALL IT+: 42 mm internal insulation Material characteristic Building material with surface coating on both sides, classification A2 – s1, d0 non-combustible Standard surface CP laminate is chemically highly stable and moisture-resitant Colour light grey, similar to RAL 7035, edges and bevels in different colour Options Door handles, locking cylinder, profile cylinder rosette Door closer Door hold-open device Panic release Electronic door closing systems Ventilation flap Cable and pipe bulkheads Stainless steel encasement 1.4571 on request Element-External dimension (H x B) in mm: ………………………………….. Surface: ………………………………….. Wall type: ………………………………….. Door stop (DIN L / DIN R): ………………………………….. Numbers of door leaf: ………………………………….. Numbers of glas elements: ………………………………….. Dimension of glas elements (H x B) in mm: ………………………………….. Numbers of fixed leaf: ………………………………….. Numbers of active leaf: ………………………………….. Connections ceiling: ………………………………….. Ceiling elements (B x T) in mm: ………………………………….. Number of PRIODOOR FSA: ………………………………….. Dimension PRIODOOR FSA (H x B) in mm: ………………………………….. Number of PRIODOOR ETX: ………………………………….. Dimension PRIODOOR ETX (H x B) in mm: ………………………………….. Options: ………………………………….. Typ: PRIOWALL IT Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |