| 10 | 1 | HSRZ High-Security Room Cell The PRIORIT High-Security Room Cell (HSRZ) is a customized room in room solution, built up of wall-, floor-, ceiling-, door-, bulkhead-, and control damper elements for used in IT- and data centers of any size, if high availability is a must. The HSRZ room system has a very high mechanical strength against extreme impact and pressure loads, also in the event of a fire. The HSRZ was tested as room solution to the stringent requirements of EN 1047 Part 2 as protection class R60D and has the ECB-S certificate. Besides the requirements of the high security level for IT protection, the HSRZ also achieve the statutory structural fire protection according to DIN 4102. Maximum IT protection + maximum IT security IT protection according to EN 1047/2 + statutory fire protection according to DIN 4102 Function Fire resistance 180 minutes (Element testing for wall, ceiling, floor) Fire resistance 90 minutes (Element testing for doors, penetration seals, damper) R 60 D classification Compliance with the limits specified in EN 1047 Part 2 ECB•S certification System test by official material testing institute Protection rating according to IP 56 Anti-burglary protection according to RC3 DIN EN 1627 Overall system verification IP 56 according to EN 60529 Protection against electromagnetic radiation Construction Room element wall, ceiling, floor, door with a very high mechanical strength ECB•S certified for highest demands Door(s) with three sealing levels Door(s) with 3D stainless steel bands, multi-locking system, profile cylinder and anti-panic function Overpressure and climate control damper Fire resistant pipe and cable bulkheads Waterproof jointing Mounting angle of galvanized steel Gasket profile Trim Material characteristic Ultra-light speciality concrete, watertight Water repellent special geomembrane, overlapping SD > 1500 mm Metallic foil coating as electromagnetic shielding Corrosion resistant steel reinforcement as burglary protection, statically effective Options Overpressure control damper Climate control damper Cable- and pipe bulkheads Customized wall facing Project-specific quotation for the High-Security Room Cell Room-Dimensions: (Height x Width x Depth) in mm: ………………………………….. Number of doors: ………………………………….. Number of cable- and and pipe bulkheads:………………………….. Number of climate control dampers: ……………………………….... Number of overpressure control dampers:……………………….….. Customise wall facing: ……………………………..….. Type: High-Security Room Cell (HSRZ) Brand: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |