| 10 | 1 | PRIODOOR FSA TUN Single and two-leaf tunnel operating doors Pressure and suction-stable door for use in company buildings, technical rooms etc. Design according to Directive 2004/54/EC, RABT, RVS, ZTV-ING part 5 and TL/TP TTT. The design considers the special requirements for technical equipment used in the operation of road tunnels in Austria. Function Fire resistance 90 minutes: fire-resistant T 90 classification Smoke-tight and tested for continuous operation Protection rating in accordance with IP 54 Stable against pressure / suction up to 2000 Pa Construction Single and double-leaf fire-resisting closure Solid door leaf with stainless steel surface on the inside and outside Circumferential block frame on three or four sides with stainless steel surface Adjustable stainless steel hinges Locking with three bolt lock Self-closing via adjustable overhead door closers (active leaf) Fixed-leaf with gate espagnolettes Multistage fire protection seal, autonomously expands in case of fire Monitorable door status by inductive proximity switch Equipotential bonding Material characteristic Building material A2 – s1, d0 non-combustible Building material is chemically highly stable, solid, stable and moisture-resistant Surface on both sides in stainless steel 1.4571, material characteristic according to ZTV-ING Part 5, requirement class I, Strike plates in stainless steel 1.4571 Scope of delivery Door PRIODOOR FSA TUN Mounting material Options Monitorable bolt contact Special sizes on request Emergency release Door closer with closing sequence control Variants – single-leaf Exterior height of element: 1811 – 2500 mm Exterior width of element: 480 – 1250 mm Variants – double-leaf Exterior height of element: 1811 – 2500 mm Exterior width of element: 480 – 2500 mm Typ: PRIODOOR FSA TUN Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |