| 10 | 1 | PRIODOOR FW TUN Tunnel Escape Door Escape door as a means of closure of escape tunnels and rescue routes. Designed according to Directive 2004/54/EG, RABT, ZTV-ING Part 5 and TL/TP TTT. The design considers the special requirements for technical equipment used in the operation of road tunnels. Function Fire resistance 90 minutes: fire-resistant T 90 classification Tested for continuous operation Stable against pressure / suction up to 1000 Pa Construction Design as a single-leaf escape door Solid door leaf with stainless steel surface on both sides Inspection window with F 90 glass Adjustable stainless steel bands with triple latch lock Self-closing doors with damped pinion door closer Door handle set on both sides in stainless steel 1.4571 Inscription with pictograms according to RABT and TL/TP TTT Monitorable door status by inductive proximity switch Equipotential bonding Material characteristic Building material A2 – s1, d0 non-combustible Building material is chemically highly stable, solid, stable and moisture-resistant Surface on both sides in stainless steel 1.4571, material characteristic according to ZTV-ING Part 5, requirement class I; powder-coated on one side in green as specified by principal Strike plates in stainless steel 1.4571 Scope of delivery PRIODOOR FW TUN escape door, pictograms, mounting material Options Electromechanical door opening assistance Special sizes on request Variants Exterior height of element (HxB) 1811 – 2500 Exterior width of element (HxB) 480 – 1250 Typ: PRIODOOR FW TUN Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |