| 10 | 1 | PRIODOOR PA3000 TUN Tunnel Special Door Pressure and suction-stable door for use with increased demands on pressure and suction stability as well as for use in the immediate vicinity of ventilation areas as a special door. Designed according to Directive 2004/54/EG, RABT, ZTV-ING Part 5 and TL/TP TTT. The design considers the special requirements for technical equipment used in the operation of road tunnels. Function Fire resistance 90 minutes: fire-resistant T 90 classification Smoke-tight and tested for continuous operation Protection rating in accordance with IP 54 Stable against pressure / suction up to 3000 Pa Construction Single-leaf fire-resisting closure Solid door leaf with stainless steel surface on the inside and outside Circumferential block frame on three or four sides with stainless steel surface Door stop optionally DIN L / DIN R Adjustable stainless steel hinges Locking with three bolt lock Self-closing via adjustable overhead door closer Multistage fire protection seal, autonomously expands in case of fire Equipotential bonding Material characteristic Building material A2 – s1, d0 non-combustible Building material is chemically highly stable, solid, stable and moisture-resistant Surface on both sides in stainless steel 1.4571, material characteristic according to ZTV-ING Part 5, requirement class I, Strike plates in stainless steel 1.4571 Scope of delivery Door PRIODOOR PA3000 Installation Instruction Options Door status monitoring with inductive proximity switch Special sizes on request Element-External dimension (H x B) in mm: ………………………………….. Rough opening (H x B) in mm: ………………………………….. Surface: ………………………………….. Weight: ………………………………….. Wall type: ………………………………….. Door stop (DIN L / DIN R): ………………………………….. Options: ………………………………….. Typ: PRIODOOR PA3000 TUN Fabrikat: PRIORIT AG www.priorit.de Tel.: 06181 / 3640 0 Fax : 06181 / 3640 230 |  |  |
| --- | --- | --- | --- | --- |